SEC. 47-18. – Specific Use Requirements

Sec. 47-18.9. - Cluster development.

A.	For the purposes of this section, a cluster development is defined as one (1) or more cluster buildings and their required amenities occurring on abutting lots.

B.	A cluster building is defined as a residential structure containing two (2), three (3), or four (4) dwelling units, which building is required to have at least one (1) shared amenity for use solely by the inhabitants of that building. Amenities may include, but are not limited to, a pool, spa, gazebo, outdoor grill, or covered terrace. Required amenities may be combined in one (1) location for use by the inhabitants of a maximum two (2) cluster buildings only when those two (2) buildings are located back-to-back.

C.	Design criteria for cluster buildings. A cluster building shall meet the following design criteria:

1.	Lot requirements. The minimum lot size for a cluster building shall be as required by the zoning district where it is located.

2.	Density. As regulated by the zoning district where the cluster development is located.

3.	Access to cluster developments shall meet the following requirements:. All units in a cluster building shall have vehicular access to a public street in the form of a private driveway. Provisions satisfactory to the city attorney shall be made for a recordable easement over the driveways for all public utilities and for use by owners within the group.

a.	Cluster buildings having a front façade abutting a public right-of-way shall only be permitted vehicular access at the rear of each unit.  No cluster building with a front façade abutting a right-of-way shall be permitted to have parking facilities for individual units directly accessed from the public right-of-way.  Access to cluster units within cluster buildings with front façades abutting a right-of-way may have access from a shared driveway.

b.	Cluster developments that abut a platted alley shall provide access from the alley.

c.	Vehicular access to a cluster development shall be provided from a public right-of-way in the form of a private driveway when no access can be provided from an alley. Provisions satisfactory to the city attorney shall be made for a recordable easement over the driveways for all public utilities and for use by owners within the group.

4.	Yard requirements.

a.	Front yard. The A cluster building abutting a public right-of-way shall provide a minimum front yard of fifteen (15) feet shall be the same as for the district where the cluster building is located. A five-foot easement along the front property line of the cluster building shall be required if the fee simple lot of each unit does not directly abut the public right-of-way. Provisions satisfactory to the city attorney shall be made for a recordable easement along the front property line of the cluster building for use by the owners of the units.

b.	Corner yards.  A cluster building abutting a public right-of-way shall provide a minimum corner yard of fifteen (15) feet. A five (5) foot easement along the corner property line of the cluster building shall be required if the fee simple lots of each unit does not directly abut the public right-of-way.  Provisions satisfactory to the city attorney shall be made for a recordable easement along the corner property line of the cluster building for use by the owners of the units.

Side yards. The minimum side yard shall be the same as required by the zoning district where the cluster building is located. The shared side yard of a cluster building shall be five (5) feet for the principal structure only. A five-foot easement which extends from front to rear lot lines along a side lot line of the cluster building not abutting a public street shall be required for use by owners within the group.

c.	Side yards. The minimum side yard shall be the same as required by the zoning district where the cluster building is located. The shared side yard of a cluster building shall be five (5) feet for the principal structure only. A five-foot easement which extends from front to rear lot lines along a side lot line of the cluster building not abutting a public right-of-way shall be required for use by owners within the group.

Rear yard. The minimum rear yard shall be as required by the zoning district where the cluster building is located. The rear yard of a single cluster building shall be fifteen (15) feet for the principal structure. Provisions satisfactory to the city attorney shall be made for a five-foot recordable easement along the rear property line of the cluster building for use by the owners of the dwelling units in that building.

d.	Rear yard. The minimum rear yard shall be as required by the zoning district where the cluster building is located. The rear yard of a single cluster building shall be fifteen (15) feet for the principal structure. Provisions satisfactory to the city attorney shall be made for a five-foot recordable easement along the rear property line of the cluster building for use by the owners of the dwelling units in that building.

Additional setbacks.

i.	A minimum of twenty-five percent (25%) of the front façade shall be set back a minimum of an additional five (5) feet from the rest of the front façade. This setback shall be centered on the building and shall have a roof line a minimum of five (5) feet lower than the highest adjacent roof line.

ii.	A minimum of twenty-five percent (25%) of the rear façade shall be set back a minimum of an additional ten (10) feet from the rest of the rear façade. This setback shall be centered on the building and shall have a roof line a minimum of five (5) feet lower than the highest adjacent roof.

iii.	Where two (2) cluster buildings share a rear property line, the minimum rear setback may be reduced to five (5) feet on each side of that rear property line if this additional portion of the building is set back an additional five (5) feet from the nearest side property line and has a roof line that is a minimum of five (5) feet lower than the highest adjacent roof line.

iv.	When any portion of a cluster building exceeds twenty-two (22) feet in height, that portion of the structure shall be set back an additional one (1) foot for each foot of height above twenty-two (22) feet.

e.	Additional setbacks.

i.	A minimum of twenty-five percent (25%) of the front façade shall be set back a minimum of an additional five (5) feet from the rest of the front façade.

ii.	A minimum of twenty-five percent (25%) of the rear façade shall be set back a minimum of an additional five (5) feet from the rest of the rear façade.

iii.	When any portion of a cluster building exceeds twenty-two (22) feet in height when abutting the side yard for the development site, that portion of the structure shall be set back an additional one (1) foot for each foot of height above twenty-two (22) feet.

5.	Architectural elements style. A cluster building shall be designed of an architectural style compatible with and complementary to adjacent structures.

a.	A cluster building shall be designed to provide a minimum of thirty (30) percent of the front façade in the form of transparent glass.

6.	Entrance requirements. Any building façade facing a public right-of-way shall be considered the front façade for those units. Each dwelling unit must have, on a front façade, its own principal entrance facing the public right-of-way. The principal entrance of each unit shall be a roofed concrete landing a minimum of three (3) feet by five (5) feet and shall be of architectural design and material similar to and integral with the principal structure. No two principal entrances shall share a roofed concrete landing. The concrete landing may encroach into the front yard an additional three (3) feet, but shall be no larger than three (3) feet by five (5) feet. A minimum of eight (8) linear feet shall be provided between entrances which are located within the same plane of the façade.

7.	Minimum floor area. Each individual dwelling unit shall have a minimum floor area of seven hundred fifty (750) square feet.

8.	Height. The maximum height shall not exceed thirty-five (35) feet. See Section 47-2, Measurements.

9.	Fence requirements. Seventy-five percent (75%) of all fences within twenty-five (25) feet of a public right-of-way must be of non-opaque materials such as vertical bars or picket fence.

10.	Maintenance agreement. A cluster development shall have a recorded maintenance agreement for the common areas.

11.	Sidewalk/street tree requirements. A cluster development shall provide the following:

a.	A minimum five-foot wide sidewalk along each public right-of-way abutting the property along the full length of the front property line.

b.	A minimum three (3) foot sidewalk consisting of pervious material subject to approval by the City Engineer shall connect the front facing entrances with the public sidewalk for those units within a cluster building that face a public right-of-way.

Street trees shall be planted and maintained along the public street abutting the property to provide a canopy effect. The type of street trees may include shade, flowering and palm trees and shall be planted at a minimum height and size in accordance with the requirements of Section 47-21, Landscape and Tree Preservation Requirements. The location and number of trees shall be determined by the department based on height, bulk, shadow, mass and design of the structures on the site and the proposed plan's compatibility to surrounding properties.

c.	Street trees shall be planted and maintained along the public right-of-way abutting the property to provide a canopy effect. The type of street trees may include shade, flowering and palm trees and shall be planted at a minimum height and size in accordance with the requirements of Section 47-21, Landscape and Tree Preservation Requirements. The location and number of trees shall be determined by the department based on building and site design, separation distance, utility infrastructure and the proposed plan's compatibility to surrounding properties.

12.	Landscape requirements. As required by the zoning district where located, pursuant to Section 47-21.10, Landscaping and Tree Preservation Requirements 47-21.13. Landscape requirements for all zoned districts.

Sec. 47-18.33. - Townhouse.

A.	Definition. For the purposes of this section, a townhouse development shall be defined as three (3) or more attached single family dwelling units where each individual single family unit and land thereunder is owned in fee simple.

B.	Site design criteria. A townhouse development shall meet the following site design criteria:

1.	Minimum lot size. The lot upon which the group is located shall contain a minimum area of seven thousand five hundred (7,500) square feet and shall provide an average of two thousand (2,000) square feet per dwelling unit, including driveways and areas held in common ownership.

2.	Density. Density shall be limited as provided for the zoning district where a townhouse development is proposed to be located.

3.	Group limit. A townhouse group shall be limited to a maximum of eight (8) dwelling units. A minimum of twenty-five percent (25%) of the townhouse group's front façade shall be set back an additional five (5) from the rest of the front façade. Attached units may have a common wall or individual sidewalls separated by a distance of not more than one (1) inch or as determined reasonable by the building inspector. If individual walls are used, the buildings shall have adequate flashing at the roofline.

4.	Access to townhouse developments shall meet the following requirements:. Each dwelling unit shall have vehicular access on a public street or paved driveway or parking area serving the group. Private driveways shall be provided in accordance with Section 47-20.5.D. Provisions satisfactory to the city attorney shall be made for a recordable easement over the driveway for all public utilities and for use by owners within the group.

a.	Each townhouse dwelling unit shall have vehicular access to a public right-of-way or paved driveway or parking area serving the group. Private driveways shall be provided in accordance with Section 47-20.5.D. Provisions satisfactory to the city attorney shall be made for a recordable easement over the driveway for all public utilities and for use by owners within the group.

b.	Townhouse developments that abut a platted alley shall provide access exclusively from the platted alley.

c.	Townhouse developments that provide for parking at the rear of townhouse units with no individual garage or driveway serving the townhouse units that abut the public right-of-way may reduce the front yard requirement to twenty (20) feet subject to the following:

i.	Townhouse units may be accessed from one (1) two-way driveway or two (2) one-way driveways; and,

ii.	Parking shall not be permitted between the townhouse buildings and any public right-of-way; and,

iii.	The area between the townhouse building and the public right-of-way shall be landscaped accept as provided herein.

5.	Yard requirements.

a.	Front yard. The minimum front yard shall be the same as that required for the zoning district where the townhouse development is located. A five-foot easement along the front property line of the group shall be required if the fee simple lot of each unit does not directly abut the public right-of-way. Provisions satisfactory to the city attorney shall be made for a recordable easement along the front property line of the group for use by the owners of the group.

b.	Side yard. The minimum side yard shall be a minimum of ten (10) feet from the side property line of the townhouse group and a minimum of twenty (20) feet measured from an ultimate right-of-way, dedicated street, or street-widening line. A five-foot easement which extends from front to rear lot lines along a side lot line of the townhouse group not abutting a public street shall be required for use by owners within the group.

c.	Rear yard. Shall be a minimum of twenty (20) feet from the rear property line. Provisions satisfactory to the city attorney shall be made for a recordable easement along the rear property line of the group for use by the owners of the group.

d.	Additional requirements. When any portion of a townhouse structure exceeds twenty-two (22) feet in height, that portion of the structure shall be set back a minimum of an additional one (1) foot for each foot of height above twenty-two (22) feet.

6.	Entrance requirements. Within the RC-15 district only, any The principal structure's façade facing a public right-of-way shall be considered the front façade for those units. Each unit must have, on a front façade, its own principal entrance facing the public right-of-way. The entrance shall be a roofed concrete landing a minimum of three (3) feet by five (5) feet and shall be of architectural design and material similar to and integral with the principal structure. No two (2) principal entrances shall share a roofed concrete landing.  The concrete landing may encroach into the front yard subject to the setback requirements of Section 47-19.2.Y. Porch, but shall be no larger than three (3) feet by five (5) feet. A minimum of eight (8) linear feet shall be provided between entrances which are located within the same plane.

7.	Minimum floor area. Each individual dwelling unit shall have a minimum floor area of seven hundred fifty (750) square feet.

8.	Height. The maximum height shall not exceed thirty-five (35) feet. See Section 47-2, Measurements.

9.	Fence requirements. Within the RC-15 district only, for new construction, seventy-five percent (75%) of all fencing along the front yard of a townhouse development abutting a public right-of-way must be of non-opaque materials such as vertical bars or picket fence, and be subject to all other requirements of Section 47-19.5, Fences, Walls and Hedges.

10.	Garages facing public rights-of-way shall be subject to the following requirements:

a.	Garages shall be limited to a width equivalent to a maximum of fifty (50) percent of the width of the townhouse unit; and,

b.	Garages shall be setback and additional five (5) feet from the principal façade of the building.

Landscape requirements. A townhouse development shall provide the following:

a.	A minimum five-foot wide sidewalk along each public street abutting the property along the full length of the front property line. A minimum three-foot wide sidewalk shall be provided from each principal entrance to the public sidewalk unless the DRC determines that alternative pedestrian access to the public sidewalk is provided.

b.	Street trees shall be planted and maintained along the public street abutting the property to provide a canopy effect. The type of street trees may include shade, flowering and palm trees and shall be planted at a minimum height and size in accordance with the requirements of Section 47-21, Landscape and Tree Preservation Requirements. The location and number of trees shall be determined by the department based on height, bulk, shadow, mass and design of the structures on the site and the proposed development's compatibility to surrounding properties.

11.	Landscape requirements. A townhouse development shall provide the following:

a.	A minimum five-foot wide sidewalk along each public right-of-way abutting the property along the full length of the front property line. A minimum three-foot wide sidewalk consisting of pervious material as approved by the City Engineer and separated from any vehicular use area shall be provided from each principal entrance to the public sidewalk unless the DRC determines that alternative pedestrian access to the public sidewalk is provided.

b.	Street trees shall be planted and maintained along the public right-of-way abutting the property to provide a canopy effect. The type of street trees may include shade, flowering and palm trees and shall be planted at a minimum height and size in accordance with the requirements of Section 47-21, Landscape and Tree Preservation Requirements. The location and number of trees shall be determined by the department based on building and site design, separation distance, utility infrastructure and the proposed plan's compatibility to surrounding properties.

Maintenance agreement. A townhouse development shall have a recorded maintenance agreement for the common areas.

12.	Maintenance agreement. A townhouse development shall have a recorded maintenance agreement for the common areas.

Duplex/Two Family Dwelling

A.	Site design criteria. A duplex or two family dwelling shall meet the following site design criteria:

1.	Entrance requirements. The principal structure's façade facing a public right-of-way shall be considered the front façade for those units. Each unit must have, on the front façade, its own principal entrance facing the public right-of-way.  The entrance shall be a roofed concrete landing a minimum of three (3) feet by five (5) feet and shall be of architectural design and material similar to and integral with the principal structure. No two (2) principal entrances shall share a roofed concrete landing.  The concrete landing may encroach into the front yard subject to the setback requirements of Section 47-19.2.Y. Porch, but shall be no larger than three (3) feet by five (5) feet. A minimum of eight (8) linear feet shall be provided between entrances.

2.	Fence requirements. For new construction, seventy-five percent (75%) of all fencing located within the front yard setback of a duplex or two family dwelling development must be of non-opaque materials such as vertical bars or picket fence, and be subject to all other requirements of Section 47-19.5, Fences, Walls and Hedges.

3. Garages facing the public right-of-way shall be subject to the following criteria:

a.	Garages shall be limited to a width equivalent a maximum of thirty (30) percent of the width of the townhouse unit; and,

b.	Garages shall be setback an additional five (5) feet from the principal façade of the building.

11.	Landscape requirements. A townhouse development shall provide the following:

a.	A minimum five-foot wide sidewalk along each public right-of-way abutting the property along the full length of the front property line.

b.	A minimum three-foot wide sidewalk will connect the front entrances with the sidewalk along the right-of-way unless the DRC determines that alternative pedestrian access to the public sidewalk is provided..

c.	Street trees shall be planted and maintained along the public right-of-way abutting the property to provide a canopy effect. The type of street trees may include shade, flowering and palm trees and shall be planted at a minimum height and size in accordance with the requirements of Section 47-21, Landscape and Tree Preservation Requirements. The location and number of trees shall be determined by the department based on building and site design, separation distance, utility infrastructure and the proposed plan's compatibility to surrounding properties.

Sec. 47-19.2. - Accessory buildings, structures and equipment, general.

…

B.	Architectural features in residential districts. Architectural features such as eaves, cornices, unenclosed balconies with open railings, window sills, awnings, chimneys, bay windows, and dormers accessory to a residential use are permitted to extend into a yard area a distance of three (3) feet from the face of the building, or one-third (1/3) of the required yard, whichever is less. Unenclosed balconies with open railings may extend into the side yards a distance of three (3) feet from the face of the building, or one-third (1/3) of the required side yard and may extend into the front yard a distance of five (5) feet from the face of the building. Accessory Excluding unenclosed balconies encroaching into the front yard, accessory uses which encroach into any yard area are permitted to have a total combined linear façade length not greater than twenty percent (20%) of the total linear length of the façade to which they are attached. Items such as windowsills or belt courses which extend six (6) inches or less into the yard area shall not be considered for the length limitation. Eaves shall not be subject to the length limitation. The dimensional limitations of this subsection shall not apply and the provisions of subsection C. shall apply to awnings accessory to a residential use in a nonresidential zoning district.

…

H.	Driveways. Driveways shall be subject to the following requirements: permitted in all zoning districts within the required front and side yards. Driveways shall be permitted in all residential zoning districts within the required rear yards only when that yard abuts a street or alley. In nonresidential zoning districts, driveways shall be permitted in any yard, except where prohibited by the ULDR. A driveway shall be a minimum of eighteen (18) feet in length when used as a stacking or a parking space. See Section 47-20, Parking and Loading Requirements.

1.	Driveways shall be permitted in all zoning districts within the required front, corner and side yards; and,

2.	Driveways shall be permitted in all residential zoning districts within the required rear yards only when the rear yard abuts a street or an alley or the driveway is in association with a townhouse, cluster, duplex, two-family home, or multifamily development; and,

3.	Driveways associated with each unit within a townhome, cluster, duplex or two family development shall have a minimum separation of eight (8) feet from neighboring driveways within the same development for the entire length of the driveway from the public right-of-way to the garage or parking space; and,

4.	In nonresidential zoning districts, driveways shall be permitted in any yard, except where prohibited by the ULDR; and,

5.	A driveway shall be a minimum of eighteen (18) feet in length when used as stacking or a parking space; and,

6.	Driveways shall meet all requirements of Section 47-20, Parking and Loading Requirements.

…

K.	Garages and carports (residential use). Garages and carports may extend into a required front yard in RD, RC and RM zoning districts when accessory to a single family dwelling but no closer than twenty (20) feet from the front property line.

…

Y.	Porch. A porch accessory to and attached to a single family dwelling that is open on at least two (2) sides with no screen enclosure permitted on the open sides may be permitted to extend into the required front yard and corner yard only when attached to a standard single family home, but shall be no closer than seventeen (17) feet from the front property line in the RS-8, RD, RC and RM in all residential zoning districts. Such porches shall be open on at least two (2) sides with no screen enclosure permitted on the open sides subject to the following criteria:

1.	A porch accessory to a single family dwelling may encroach into the required front yard, but shall be no closer than seventeen (17) feet from the front property line;

2.	A porch accessory to an attached single family dwelling may encroach into the required front yard, but no closer than seventeen (17) feet and shall be limited to a maximum of three (3) feet by five (5) feet.

Sec. 47-20.13. - Paving and drainage.

A.	Paving. Except as provided in subsections B and C, off-street parking facilities and spaces, including aisles and driveways, shall at a minimum be surfaced with a hard, dust free material, at least one (1) inch thick asphaltic cement on at least six (6) inch compacted limerock base course compacted to an average density not less than ninety-eight percent (98%) of the maximum density obtainable under the test provided pursuant to engineering standard (AASHTO T-180) or an equivalent test. The minimum density which will be acceptable at any location within the base shall be ninety-six percent (96%) of such maximum density and, in the determination of average density, the maximum density which shall be used in the calculation shall be one hundred two percent (102%). Other equivalent pavement systems which will support the intended use may be approved by the city engineer. All pavement systems shall be maintained in a smooth, well-graded condition.

B.	Parking spaces and facilities for single family uses may have a gravel surface.

C.	Parking facilities and spaces for public and private schools offering academic courses, houses of worship, and public recreational uses when use of the lots is limited to three (3) days of the week or less may be grass over a compacted subsurface. Grass parking surfaces shall consist of at least a six (6) inch course of natural limerock, surfaced with a species of grass acceptable for high-traffic use. Other equivalent surfaces may be approved by the city engineer. The parking area shall have adequate drainage as provided herein. All requirements for landscaping vehicular use areas shall be met as well as all required interior landscaping requirements for parking areas. Grass parking areas shall not count toward satisfying any landscaping area required by Section 47-21, Landscape and Tree Preservation Requirements.

D.	Drainage. On-site stormwater retention shall be provided in accordance with the requirements of the regulatory authority with jurisdiction over stormwater retention.

E.	Paving in the right-of-way may only be installed in association with on-street public parking or for driveways to provide vehicular ingress/egress subject to the minimum area necessary to provide for safe ingress/egress to the private property. Whenever the total pavement area in the swale area frontage on public right-of-way is fifty percent (50%) or more of the total frontage on that public right-of-way a french drain stormwater system in the swale area in accordance with city construction standards and specifications will be required. When the adequacy of the existing storm drain facilities can be certified by a licensed engineer this requirement may be waived by the city engineer.

Sec. 47-21.14. - Additional landscape requirements for special uses and districts.

A.	In addition to the requirements for land zoned in certain districts, additional landscaping shall be required for certain special districts and uses as follows:

1.	Downtown Regional Activity Center (RAC).

a.	Within the RAC districts newly planted street trees shall be limited to the following species:

| RAC Street | Tree Species* |
| --- | --- |
| Broward Boulevard | Royal Palm (Roystonia elata) |
| Andrews Avenue | Sabal Palm (Sabal palmetto) Carpentaria Palm (Carpentaria acuminata) |
| Federal Highway | Sabal Palm (Sabal palmetto) Gumbo Limbo (Bursera simarouba) Live Oak (Quercus virginiana) Weeping Wild Tamarind (Lysiloma sabicu) |
| East 8th Avenue | No designated tree |
| East 3rd Avenue | Royal Palm (Roystonia elata) Live Oak (Quercus virginiana) Carpentaria Palm (Carpentaria acuminata) |
| East 1st Avenue | Gumbo Limbo (Bursera simarouba) |
| West 1st Avenue | No designated tree |
| West 3rd Avenue | No designated tree |
| Flagler | Live Oak (Quercus virginiana) |
| West 2nd Avenue | Little Leaf Calophyllum (Calophyllum antillarum) |
| West 4th Avenue | Live Oak (Quercus virginiana) |
| West 5th Avenue | Live Oak (Quercus virginiana) |
| South 7th Street | No designated tree |
| East South 6th Street | Royal Palm (Roystonia elata) |
| West South 6th Street | No designated tree |
| South 5 Street | No designated tree |
| S.E. 5th Court | Gumbo Limbo (Bursera simarouba) Maypan Palm (Cocos nucifera var. Maypan) |
| S.E. 4th Street | Weeping Wild Tamarind (Lysiloma sabicu) |
| Las Olas Boulevard | Sabal Palm (Sabal palmetto) Live Oak (Quercus virginiana) Maypan Palm (Cocos nuciefer var. Maypan) Carpentaria Palm (Carpentaria acuminata) |
| South 2nd Street, east of city parking garage | Royal Poinciana (Delonix regia) Live Oak (Quercus virginiana) |
| South 2nd Street, west of city parking garage | Weeping Wild Tamarind (Lysiloma sabicu) Sabal Palm (Sabal palmetto) |
| South 1st Street | No designated tree |
| North 1st Street | No designated tree |
| North 2nd Street | Live Oak (Quercus virginiana) Washington Palm (Washingtonia robusta) |
| North 3rd Street | Weeping Wild Tamarind (Lysiloma sabicu) |
| North 4th Street | Gumbo Limbo (Bursera simarouba) |
| North 5th Street | No designated tree |

*Black Olive (Bucida buceras) trees existing as street trees prior to March 26, 1999 are legal and their existence shall not cause a development to be nonconforming, and shall be considered to meet the street tree requirements for any redevelopment or reconstruction of existing structures adjacent to or in front of said Black Olive trees, but such trees shall not be permitted to be planted or replaced with Black Olive subsequent to this date.

b.	When planted in non-pervious areas, dicot street trees shall be accompanied by expandable tree grates or porous aggregate system which are at least five (5) feet square, with three-eighths (3/8) inch slot openings. Area must meet current ADA standards.

c.	All newly planted dicot street trees shall have a minimum caliper of two and one half (2½) inches.

d.	All newly planted monocot street trees shall have a minimum overall height of twelve (12) feet.

e.	Planting plans shall obtain the approval of the department. The necessity for installation of an irrigation system for street trees and the type and kind to be used shall be determined by the city based on tree species requirements.

f.	The RAC requirements may be appealed by written request to the department. Such appeal shall be accompanied by a plan which shows the location, size, description and species of landscape improvements proposed. The department may find that the applicant is unable to observe planting requirements for reasons such as the lack of available plant material, constraints of the planting area or inconsistency with existing street trees or building design. In the department's discretion, when the appeal provides landscaping which is harmonious with adjacent landscaping and uses and is otherwise consistent with the intent and purpose of this subsection, they may approve modifications to Code requirements.

2.	Signs. The landscape area required by the sign regulations of this chapter shall be planted with shrubs or ground cover. Asphalt and rock shall be removed and the area refilled with clean, fertile soil, as necessary, before planting. The area shall be protected from vehicle encroachment by a barrier placed around the outside edge of the required landscape area.

3.	Townhouse developments/zero-lot-line homes/cluster dwellings shall be subject to the following requirements:. Land which is common area for a townhouse complex or cluster complex shall have the same open space and planting requirements as the district in which it is located. Individual lots owned in fee simple by individual owners in a townhouse development, zero-lot-line development or cluster development shall have the same planting requirements as in the RS-4.4 district.

a.	Land which is common area for a townhouse development or cluster development shall have the same open space and planting requirements as the district in which it is located;

b.	The rear of individual lots owned in fee simple by individual owners of a townhouse development, zero-lot-line development or cluster development shall be exempt from the requirements to provide landscape area, however all hardscapes shall consist of pervious materials subject approval by the City Engineer.

4.	Parking garages.

a.	Structures which enclose parking shall provide a landscape area between the street and that portion of structure enclosing the parking utilizing trees and ground cover. The minimum square footage of the landscape area to be provided shall be determined by multiplying by five (5) the lineal street frontage of the parcel of land upon which the parking garage is located, and adding four hundred (400) square feet for each corner of the parcels adjacent to a street.

b.	Parking garages constructed in residentially-zoned districts shall meet the landscape requirement of the district in which the garage is located. No paving or walkways shall be allowed in the yard fronting on the principal street other than necessary access from that right-of-way.

5.	House of worship. The landscaping requirements for a house of worship shall be the same as the zoning district in which the house of worship is located. VUA landscaping shall be required. A landscaping irrigation system shall be installed.

6.	Backout parking. Except when used for a single family dwelling, when a parcel of land has a VUA designed to permit motor vehicles to back directly out onto a public right-of-way, including an alley, a landscape area at the front of the parking spaces unobstructed by a fence or wall shall be provided. The landscape area shall be a minimum of five (5) feet in width and shall contain not less than ten (10) square feet for each linear foot of VUA fronting on the street. The landscaping for this area shall consist of hedges and trees. There shall be no more than two (2) parking spaces in a row without a tree island when the parking serves a residential or hotel/motel use, and no more than four (4) parking spaces in a row without a tree island when the parking serves any other use. A poured six (6) inch high concrete curb shall be placed across the nose of tree islands.

7.	Noncontiguous parking lots.

a.	Freestanding, noncontiguous, or remote VUAs shall be landscaped according to minimum VUA requirements and maintained by an irrigation system.

b.	The parcel shall contain no dumpster or structures other than fences, walls or lights poles. If a dumpster or structure is located on the property, the requirements of the zoning district where the VUA is located shall apply.

8.	Fences and walls. On a parcel of land in a non-residential district, when a fence or wall is located adjacent to a street, it shall be subject to the requirements of Section 47-19.5.

9.	Bufferyard requirement. The landscape area required by bufferyard requirement as provided in Section 47-25.3, Neighborhood Compatibility Requirements, is intended to provide a heavily-vegetated view from the residential parcel. The tree requirements for the bufferyard are in addition to trees required to be installed to comply with general tree planting requirements and trees required for a VUA and include a minimum of one (1) tree for every three hundred (300) square feet or fraction thereof of bufferyard area. Trees shall be dicot types obtaining a fifteen-foot minimum height at maturity as listed in the table of tree evaluation and monocots obtaining a twelve-foot minimum height at maturity. The species mix shall be at least two-thirds (2/3) dicots.

10.	Self storage/mini warehouse facility. The twenty-foot yard required as provided in Section 47-18.29 shall be in landscaping. A vehicular use area may also be located between the structure and street and may divide the landscape area as long as there is a total of twenty (20) feet in landscape area. This twenty (20) feet landscape area may be used to meet the landscape area required pursuant to Section 47-18.29.